## Slide 1
大地測量資料庫
童 忻
Hsin Tung
中央研究院 地球科學研究所
Academia sinica Institute of Earth Sciences

## Slide 2
How to measure Earth’s surface (change)?
Courtesy of Ray Y. Chuang

## Slide 3
Courtesy of Ray Y. Chuang

## Slide 4
Courtesy of Ray Y. Chuang

## Slide 5
Courtesy of Ray Y. Chuang

## Slide 6
Velocity Field (2010-2025)

## Slide 7
Coseismic displacement (2024/04/03 event)

## Slide 8: What is GPS?
The global positioning system is a satellite-based navigation system consisting of a network of 24 orbiting satellites that are eleven thousand nautical miles in space and in six different orbital paths. The satellites are constantly moving, making two complete orbits around the Earth in just under 24 hours.
The GPS project was started by the U.S. Department of Defense in 1973. The first prototype spacecraft was launched in 1978 and the full constellation of 24 satellites became operational in 1993.
Originally limited to use by the United States military, civilian use was allowed from the 1980s.
wikipedia

## Slide 9: GNSS : Global Navigation Satellite System
GPS (USA)
GLONASS (Russia)
QZSS (Japan)
Galileo (EU)
Beidou (China)
Not only GPS !

## Slide 10: The GPS System

## Slide 11: GPS User Segment
5 – 10 m <1- 10 m 1 mm to 1 cm
3 – 10 K NTD 30 – 100 K NTD > 200 K NTD

## Slide 12: Taiwan GNSS Array
Since 1990
Total : 540+
Working : 400+
CWA 中央氣象署
GSMMA 地礦中心
IES 中央研究院
MOI 國土測繪中心
TVO 大屯火山觀測站
WRA 水利署

## Slide 13
NTUC
S105
KNKO
SCHN
S01R
S012
operational
GPS stations

## Slide 14: GPS Time Series
1. Interseismic motion
2. Coseismic displacement
3. Postseismic displacement
4. Fault transients
5. Seasonal motion
( fault creep, water cycle, slow‐creeping landslide,
vegetation change, etc. )
(Rousset et al,. 2012)

## Slide 15
Position & Linear Rate
Annual and semi-annual periodic motion
offsets
Exponential decay
Errors
(Nikolaidis et al., 2001)
n : daily solution epochs in units of years
b : linear rate during inter-seismic period
c.d.e.f : amplitude of annual and semi-annual motions
g : offsets (including coseismic displacements and antenna changes)
h : post-seismic represent as exponential decay with magnitude
H : Heaviside step function
τ : relaxation time.
Tj : selected earthquake epochs
vi : error

## Slide 16: GPS Time Series in Matrix Form (d = Gm)
d = m G
=
觀測向量
參數向量
設計矩陣

## Slide 18
Interseismic motion

## Slide 19: Coseismic displacement

## Slide 20: Postseismic displacement

## Slide 21: Fault transients

## Slide 22
1. Fault slip at a depth range of 20-40 km
2. The slip period is about a month with a release
seismic moment equivalent of Mw 6.6
3. The recurrence interval is about 0.5 year
(Heki and Kataoka, 2008)
Yonaguni
Iriomote
Ishigaki
Miyako
Hateruma
GPS station on Hateruma island

## Slide 23: Seasonal motion

## Slide 24
Slow creeping landslides
(Hsu et al., 2014)

## Slide 25
(Hsu et al., 2014)

## Slide 26
Environmental change

## Slide 30
V2
2018 - 2022
V2
2008 - 2018

## Slide 40: Satellite visibility
Open sky
heavily
vegetated
building
obstruction
The GNSS satellite travel time diagram illustrates the distribution of satellite travel time observed at a station throughout the observation period. In areas with clear sky visibility and minimal obstructions, one would expect a higher count of visible satellites during the observation period.

## Slide 42
GNSS各分量標準偏差

## Slide 49
https://tgm.earth.sinica.edu.tw/

## Slide 50: Typical Raw data formats
Courtesy of Wang, Y.

## Slide 51: RINEX file
Receiver Independent Exchange Format
Developed by the Astronomical Institute of the university of Berne in 1989, for the easy exchange of the GPS data
The widely used format of GNSS data collection and data process (RINEX 2.x and RINEX 3.x)
The data can be compressed, or remain in ASCII format
RINEX consists of at least three sub-file type:
Observation data (.o; .obs, .yyo)
Navigation message (.n; .nav; .yyn)
Meteorological data (.m; .met; .yym)

## Slide 52: Observation file
The details of rinex header depends on the program and receiver, and person who process data !

## Slide 53
C1, Range
L1, Cycle
P2, Range
L2, Cycle
Condition of measurement

## Slide 54: Rinex ver. 3
G: GPS
R: GLONASS
E: Galileo
J: QZSS
S: SBAS payload
C: Beidou
RINEX v.3 has been extended to include more observation and frequency!!

## Slide 55
Filename
Rinex 2 :
ALGO1600.12O
Rinex 3 : ALGO00CAN_R_20121601000_01D_30S_MO.rnx
ALGO00CAN_R_20121600000_01D_GN.rnx

## Slide 56: Common post-processing software
Bernese (commercial software)
http://www.bernese.unibe.ch/
GAMIT/GLOBK (MIT)
http://geoweb.mit.edu/gg/
Relative Positioning
GIPSY-OASIS / GipsyX (JPL)
https://gipsy-oasis.jpl.nasa.gov/
RTKLIB (open source program)
http://www.rtklib.com/

## Slide 57: Online GNSS post-processing service
Geoscience Australia
AUSPOS online GPS processing service
http://www.ga.gov.au/bin/gps.pl
NOAA
OPUS: Online Positioning User Service
https://www.ngs.noaa.gov/OPUS/
JPL
The Global Differential GPS (GDGPS) System
http://www.gdgps.net/

## Slide 58
https://sideshow.jpl.nasa.gov/post/series.html

## Slide 60
http://garner.ucsd.edu/

## Slide 61
https://tgm.earth.sinica.edu.tw/